## Slide 1
Dyson – AS-IS Architecture Understanding
Notes: Note:
Dyson has their AWS accounts
The on-prem and AWS are connected through SD-WAN
They can create a new AWS account under OU but they will note share the TGW with that new account as per their company policy, So we decided to use existing account which is Non Prod RDD

## Slide 2
Networking & On-prem to AWS Connectivity
HPC & Sizing Details
Use Cases, Workstations and Sizing Details
Authentication
Success Criteria
Design/Architecture to meet the requirement
Dyson – AS-IS Model
Notes: Note:
Dyson has their AWS accounts
The on-prem and AWS are connected through SD-WAN
They can create a new AWS account under OU but they will note share the TGW with that new account as per their company policy, So we decided to use existing account which is Non Prod RDD

## Slide 3
Dyson – Networking & On-Prem to AWS Connectivity
Non Prod RDD
TGW
Proposed New VPC
Notes: Note:
Dyson has their AWS accounts
The on-prem and AWS are connected through SD-WAN
They can create a new AWS account under OU but they will note share the TGW with that new account as per their company policy, So we decided to use existing account which is Non Prod RDD

## Slide 4
Dyson – On-prem HPC
Azure AD
Notes: Note::
Dyson has HPC cluster in Malmesbury and Hullavington
Dyson users are using their desk to access the HPC cluster
Dyson users are logged in using the AD based on Azure-AD
Which domain they joined their workstation is yet to receive.
Users are using the NFS as their storage

## Slide 5
Info | HPC-01 | HPC-02
Location | Malmesbury | Hullavington
Number of Active Users | 50 | 
Number of All Users | 100 | 
Compute nodes |  | 
Nodes | 512 | 1024
Cores* per node | 16 | 
CPU info | Intel(R) Xeon(R) CPU E5-2667 v2 @ 3.30GHz | 
RAM per node [GB] | 125 | 
Total Storage [TB] | 3.46 | 
Internal Connectivity | FDR InfiniBand | 
External Connectivity | Gigabit Ethernet up to 0.1Gbps | 
Master nodes |  | 
CPU info | 2 x Intel(R) Xeon(R) CPU E5-2450 v2 @ 2.50GHz | 2 x Intel(R) Xeon(R) CPU E5-2680 v2 @ 2.80GHz
Cores* | 2 x 10 | 2 x 8
RAM [GB] | 125 | 157
Dyson – On-prem HPC Sizing Details
Notes: Note:
Currently LSF is being used as the job scheduler in their on-prem HPC

## Slide 6
Use Case | System Requirement | 
CFD DOE Optimization (FCR) | Workstation | HPC
 | CPU: 44 RAM: 256 GB Storage: 500 GB (temporary) | CPU: 32 RAM: 64 GB Storage: 200GB/Simulation 400GB/Concurrent simulation
 | Software | 
 | ANSYS Workbench ANSYS OptiSLang Siemens TeamCenter Siemens NX ANSYS-NX Plugin ANSYS Meshing ANSYS Fluent ANSYS CFD Post ANSYS RSM WinScp | ANSYS Meshing ANSYS Fluent ANSYS CFD Post
Dyson – Use Case1, Workstation & Sizing Details

## Slide 7
Use Case | System Requirement | 
Aero-Acoustic CFD (TR) | Workstation | HPC
 | CPU: 32 RAM: 128 GB Storage: 150 GB (temporary) | CPU: 256 RAM: 80 GB Storage: 150GB (temporary)
 | Software | 
 | ANSYS Workbench Siemens TeamCenter Siemens NX ANSYS-NX Plugin ANSYS Meshing/Fluent Meshing ANSYS Fluent ANSYS CFD Post WinScp Putty/Plink ANSYS RSM | ANSYS Meshing ANSYS Fluent Meshing ANSYS Fluent
Dyson – Use Case2, Workstation & Sizing Details

## Slide 8
Use Case | System Requirement | 
Transient CFD Simulation (FCR) | Workstation | HPC
 | CPU: 32 RAM: 128 GB Storage: 150 GB (temporary) | CPU: 256 RAM: 80 GB Storage: 150GB (temporary)
 | Software | 
 | ANSYS Workbench Siemens TeamCenter Siemens NX ANSYS-NX Plugin ANSYS Meshing/Fluent Meshing ANSYS Fluent ANSYS CFD Post WinScp Putty/Plink ANSYS RSM | ANSYS Meshing ANSYS Fluent Meshing ANSYS Fluent
Dyson – Use Case3, Workstation & Sizing Details

## Slide 9
Use Case | System Requirement | 
AeroAcoustic Dassault Systems CLOUD (Tech Research) | Workstation | HPC
 | Yet to receive | Yet to receive
 | Software | 
 | Yet to receive | Yet to receive
Dyson – Use Case4, Workstation & Sizing Details

## Slide 10
Dyson – Authentication
TCS Dev Center
Engineer with Dyson Laptop
Client VPN
Azure AD
Master Account
Policies
AWS SSO
Roles
Sub Account -1
Sub Account -2
VPN Solution
SD-WAN
Customer Gateway
Notes: Note:
Dyson has their AWS accounts
The on-prem and AWS are connected through SD-WAN
Azure AD is being used for the AD which is already integrated with Master A/C’s SSO, and the SSO based validation is being done for the other sub accounts
Which domain they joined their workstation is yet to receive.

## Slide 11
Dyson – Success Criteria
1 | Connection speed from Dyson to virtual workstation has to be satisfactory
2 | Users should be able to select different size of workstation up to 32 cores and 256GB RAM
3 | User should easily Hybernate/Dehybernate their workstations
4 | File transfer from Dyson to AWS platform and back at least 100MBps (ideally >200MBps)
5 | File transfer between virtual workstation and compute node has to be >1GBps
6 | HPC speed should be at least same compared the current HPC for CFD test case
7 | Platform should be scalable with number of CPUs in the same way as on the current HPC
8 | System should handle traffic with up to 100 users remoting from Dyson to the platform
9 | User should connect to Dyson network drives
10 | User should check out Dyson software licenses
11 | Data storage should be backed up for workstations and HPC
12 | HPC speed should be 1.5x better than the current HPC for CFD test case
13 | User should access software versions aligned with current usage at Dyson
14 | Automated ANSYS Workflow: User should connect from dyson to the HPC via RSM
15 | Simple ANSYS Simulation: User should be able to execute the given uses cases in VW and HPC
16 | PowerFLOW Workflow: User should be able to run benchmark DDM motor PowerFLOW sim on HPC up to 256 cores/max HPC cores. Check wall-clock / Validity of results
17 | PowerFLOW Workflow: User should be able to run automated post-processing of benchmark DDM case on Virtual workstation
Notes: Note:
Dyson has their AWS accounts
The on-prem and AWS are connected through SD-WAN
They can create a new AWS account under OU but they will note share the TGW with that new account as per their company policy, So we decided to use existing account which is Non Prod RDD

## Slide 12
Dyson – To-Be Model
Advice and proposal
SOCA vs AWS Parallel Cluster – Parallel Cluster has been finalized
Job Scheduler: LSF vs PBS vs Slurm
AWS SSO integration, Domain join
Connectivity between on-prem and AWS
Storage: FSx vs EFS
Head Node, Compute Node, Workstation Node
Performance
  Network Performance, Latency
  Compute Node Performance
  Workstation Performance
  EFA

## Slide 13
Dyson To-Be Model – Compute, Sizing, Authentication Details
Service type | Description | Qty
Compute Node | c6i.32xlarge: RHEL, 128 vCPU, 256 GiB RAM, Support EFA | On-demand
Head / Login Node | hpc6a.48xlarge:RHEL, 128 vCPU, 512 GiB RAM, Support EFA | 1
EnginFrame Portal Node | m5.24xlarge: RHEL, 96 vCPU, 384 GiB RAM | 1
Workstation | g4dn.2xlarge: Windows: 32 vCPU, 128 GiB RAM, 900 GB Local Storage | 2
Storage Accounts | FSx for Netapp Ontap | 150TB
Backup | FSx backup | 
Other Features | SD-WAN, AWS KMS, CloudWatch, AWS IAM As per requirement | 
Authentication | Azure AD and AWS SSO will be used for authentication | 
Scheduler | Existing: LSF, Proposed: PBS/Slurn | 1

## Slide 14: Dyson To-Be – High Level Architecture Diagram using Parallel Cluster (Reference Architecture)
Notes: Note:
Can you skip the LoadBalancer in PoC phase?

## Slide 15
Dyson To-Be – AWS Connectivity with On-prem and TCS Development Center
SD-WAN
Internet Gateway
Transit Account
Corp Subnet
Transit VPC
NPR RDD Account
HPC-VPC
Transit
Gateway
Cisco CSR
End Users
Dyson Malmesbury
Customer Gateway
Other-VPC
AZ-1
AZ-2
Client VPN
SD-WAN
Internet Gateway
Transit Account
Corp Subnet
Transit VPC
NPR RDD Account
HPC-VPC
Transit
Gateway
Cisco CSR
Other-VPC
AZ-1
AZ-2
Dyson Malmesbury
VPN Solution
User
Ireland Region
Ireland Region
TCS Dev Center
Cloud Engineer with Dyson Laptop
Notes: Question to Steve/Aruneet:
Can we install the entire SOCA cluster in private subnet including the head node? By changing the script
How can we change the Head Node configuration in case we need a higher sizing? By changing the script
How to create and use FSx Luster storage as the file system for the SOCA? By changing the script
How can we authenticate user’s credential based on the Azure AD (i.e. Current Dyson is using for their on-prem user)? By changing the script
Certificate Mgr can be associated later.

## Slide 16
Private subnet2
Private subnet1
Dyson To-Be – High Level Architecture Diagram using AWS Parallel Cluster – Multi-AZ
CloudWatch
Security Hub
Inspector
CloudTrail
KMS
IAM
SSO
Dir Service
HPC
AZ-1
Dyson Malmesbury
AZ-3
Private subnet3
Cloud9 is used for deployment purpose in PoC phase
HPC Instance Type
Compute: C6i.32xlarge
Head: C6i.2xlarge
Workstations
G4dn.8xlarge
Storage
Local 1 TB GP3
Shared 20 TB FSx for NetApp ONTAP
TCS Dev Center
Cloud Engineer with Dyson Laptop
TGW
Client VPN
AZ-2
Identity, Security & Compliance
Secrets Mgr
Storage Options
FSx for ONTAP
S3
SD-WAN
Cloud9
Transit Account
Corp Subnet
Internet Gateway
Cisco CSR
RDD A/C
Ireland Region
VPN Solution
User
Head Node (CentOS 7)
Scheduler
C6i.2xlarge
Workstation-1 (Windows)
Workstatio-2 (Windows)
Workstation-3 (Windows)
Workstation-4 (Windows)
Compute Nodes
Compute Nodes
Compute Nodes
Compute Nodes
Compute Nodes
Compute Nodes
Compute Nodes
Compute Nodes
Compute Nodes
Job Queues
Customer Gateway
On-prem Servers
sg-hpc-poc-cloud9
sg-hpc-poc-workstation
sg-hpc-poc-head-node
sg-hpc-poc-compute
Security Groups
Notes: Note:
The total cluster will be created in private subnets spanning across three AZs
Workstations, HeadNode will be connected to On-Prem network though SD-WAN, TGW and Domain join
Workstations: Windows 10, HeadNode: Ubuntu 20.04, On-Demand compute Node: ???
FSx Luster storage will be used
Job Scheduler Slurm will be used, however LSF is preferred
How many Job queues we should have?
Do we have any interface (i.e. similar to SOCA) to create the Workstation?
Is only One HeadNode is sufficient in the PoC phase?
Can we make it a single region, 3 AZ, without the LoadBalancer in PoC phase?
Onprem connectivity and Domain Join is required to connect the On-prem License server, NFS, PLM server
How to create the Nodes considering the Dyson domain join security requirement
What should be CIDR ranges? Is 255 IP range is OK for the PoC?
How many maximum compute node we are expecting to complete the given use cases, based on that we can ask Dyson to allow the CIDR ranges
How to do we scan the compute nodes against Qualys if that will come as a mandate?

## Slide 17
rdd-npr-hpc-1a-sn1
Dyson To-Be – High Level Architecture Diagram using AWS Parallel Cluster – Single AZ
CloudWatch
Security Hub
Inspector
CloudTrail
KMS
IAM
SSO
Dir Service
HPC
eu-west-1a
Dyson Malmesbury
Cloud9 is used for deployment purpose in PoC phase
HPC Instance Type
Compute: C6i.32xlarge
Head: C6i.2xlarge
Workstations
G4dn.8xlarge
Storage
Local 1 TB GP3
Shared 20 TB FSx for NetApp ONTAP
TCS Dev Center
Cloud Engineer with Dyson Laptop
TGW
Client VPN
Identity, Security & Compliance
Secrets Mgr
Storage Options
FSx for ONTAP
S3
SD-WAN
Cloud9
Transit Account
Corp Subnet
Internet Gateway
Cisco CSR
RDD NPR A/C
Ireland Region
VPN Solution
User
Head Node (CentOS 7)
Scheduler
C6i.2xlarge
Compute Nodes
Compute Nodes
Compute Nodes
Job Queues
Customer Gateway
On-prem Servers
sg-hpc-poc-cloud9
sg-hpc-poc-workstation
sg-hpc-poc-head-node
sg-hpc-poc-compute
Security Groups
FSx NetApp for ONTAP
sg-hpc-poc-compute-node
sg-hpc-poc-head-node
sg-hpc-poc-cloud9
Workstation-2 (Windows)
Workstation-3 (Windows)
Workstation-4 (Windows)
Workstation-1 (Windows)
sg-hpc-poc-workstation-node
Notes: Note:
The total cluster will be created in private subnets spanning across three AZs
Workstations, HeadNode will be connected to On-Prem network though SD-WAN, TGW and Domain join
Workstations: Windows 10, HeadNode: Ubuntu 20.04, On-Demand compute Node: ???
FSx Luster storage will be used
Job Scheduler Slurm will be used, however LSF is preferred
How many Job queues we should have?
Do we have any interface (i.e. similar to SOCA) to create the Workstation?
Is only One HeadNode is sufficient in the PoC phase?
Can we make it a single region, 3 AZ, without the LoadBalancer in PoC phase?
Onprem connectivity and Domain Join is required to connect the On-prem License server, NFS, PLM server
How to create the Nodes considering the Dyson domain join security requirement
What should be CIDR ranges? Is 255 IP range is OK for the PoC?
How many maximum compute node we are expecting to complete the given use cases, based on that we can ask Dyson to allow the CIDR ranges
How to do we scan the compute nodes against Qualys if that will come as a mandate?

## Slide 18
rdd-prd-hpc-euw1-1b-sn1
rdd-prd-hpc-euw1-1a-sn1
Dyson To-Be – High Level Architecture Diagram using AWS Parallel Cluster – Two AZ
CloudWatch
Security Hub
Inspector
CloudTrail
KMS
IAM
SSO
Dir Service
HPC
eu-west-1a
Dyson Malmesbury
HPC Instance Type
Compute: C6i.32xlarge
Head: C6i.2xlarge
Workstations
G4dn.2xlarge
Storage
Local 600 BB GP3
Shared 20 TB FSx for NetApp ONTAP
TCS Dev Center
Cloud Engineer with Dyson Laptop
TGW
Client VPN
Identity, Security & Compliance
Secrets Mgr
Storage Options
FSx for ONTAP
S3
SD-WAN
Transit Account
Corp Subnet
Internet Gateway
Cisco CSR
RDD PRD A/C
Ireland Region
VPN Solution
User
Job Queues
Customer Gateway
On-prem Servers
sg-rdd-prd-hpc-euw1-workstation
sg-hpc-head-node
sg-hpc-compute
sg-rdd-prd-hpc-euw1-fsx
Security Groups
FSx NetApp for ONTAP
sg-hpc-compute-node
sg-rdd-prd-hpc-euw1-fsx
Compute Nodes
Compute Nodes
Compute Nodes
Compute Nodes
Compute Nodes
Compute Nodes
Head Node (CentOS 7)
Scheduler
C6i.2xlarge
sg-hpc-head-node
Workstations (Windows)
sg-rdd-prd-hpc-euw1-workstation
Workstations (Windows)
Notes: Note:
The total cluster will be created in private subnets spanning across three AZs
Workstations, HeadNode will be connected to On-Prem network though SD-WAN, TGW and Domain join
Workstations: Windows 10, HeadNode: Ubuntu 20.04, On-Demand compute Node: ???
FSx Luster storage will be used
Job Scheduler Slurm will be used, however LSF is preferred
How many Job queues we should have?
Do we have any interface (i.e. similar to SOCA) to create the Workstation?
Is only One HeadNode is sufficient in the PoC phase?
Can we make it a single region, 3 AZ, without the LoadBalancer in PoC phase?
Onprem connectivity and Domain Join is required to connect the On-prem License server, NFS, PLM server
How to create the Nodes considering the Dyson domain join security requirement
What should be CIDR ranges? Is 255 IP range is OK for the PoC?
How many maximum compute node we are expecting to complete the given use cases, based on that we can ask Dyson to allow the CIDR ranges
How to do we scan the compute nodes against Qualys if that will come as a mandate?

## Slide 19
rdd-prd-hpc-euw1-1b-sn1
rdd-prd-hpc-euw1-1a-sn1
Dyson To-Be – High Level Architecture Diagram using AWS Parallel Cluster – Two AZ, Four Subnet
CloudWatch
Security Hub
Inspector
CloudTrail
KMS
IAM
SSO
Dir Service
HPC
eu-west-1a
Dyson Malmesbury
One Parallel Cluster Per AZ
HPC Instance Type
Compute: C6i.32xlarge
Head: C6i.2xlarge
Workstations
G4dn.2xlarge
Storage
Local 600 GB GP3
Shared 50 TB FSx for NetApp ONTAP
TCS Dev Center
Cloud Engineer with Dyson Laptop
TGW
Client VPN
Identity, Security & Compliance
Secrets Mgr
Storage Options
FSx for ONTAP
S3
SD-WAN
Transit Account
Corp Subnet
Internet Gateway
Cisco CSR
RDD PRD A/C
Ireland Region
VPN Solution
User
Job Queues
Customer Gateway
On-prem Servers
sg-hpc-workstation
sg-hpc-head-node
sg-hpc-compute
sg-hpc-fsx
Security Groups
sg-hpc-compute-node
sg-rdd-prd-hpc-euw1-fsx
Compute Nodes
Compute Nodes
Compute Nodes
Compute Nodes
Head Node-2(RHEL)
Scheduler
C6i.2xlarge
sg-hpc-head-node
Workstations (Windows)
sg-rdd-prd-hpc-euw1-workstation
eu-west-1b
FSx NetApp for ONTAP
Head Node-1(RHEL)
Scheduler
C6i.2xlarge
sg-hpc-head-node
sg-hpc-compute-node
Job Queues
Compute Nodes
Compute Nodes
Notes: Note:
The total cluster will be created in private subnets spanning across three AZs
Workstations, HeadNode will be connected to On-Prem network though SD-WAN, TGW and Domain join
Workstations: Windows 10, HeadNode: Ubuntu 20.04, On-Demand compute Node: ???
FSx Luster storage will be used
Job Scheduler Slurm will be used, however LSF is preferred
How many Job queues we should have?
Do we have any interface (i.e. similar to SOCA) to create the Workstation?
Is only One HeadNode is sufficient in the PoC phase?
Can we make it a single region, 3 AZ, without the LoadBalancer in PoC phase?
Onprem connectivity and Domain Join is required to connect the On-prem License server, NFS, PLM server
How to create the Nodes considering the Dyson domain join security requirement
What should be CIDR ranges? Is 255 IP range is OK for the PoC?
How many maximum compute node we are expecting to complete the given use cases, based on that we can ask Dyson to allow the CIDR ranges
How to do we scan the compute nodes against Qualys if that will come as a mandate?

## Slide 20
Change from PoC to Prod
System Change |  | 
Area | PoC | Prod
Base Infrastructure | New VPC, One AZ, One Subnet | New VPC, Two AZ, Two Subnet
Parallel Cluster | CentOS based | RHEL based
Shared Storage | FSx with single AZ, 20 TB, 256 MBps | FSx with multi AZ, 50 TB, 512 MBps
Security Groups | Everything Open from 10.0.0.0/8 | Specific IP, Port to open from London and Singapore IP breakout
Workstation Security | All allowed from 10.0.0.0/8 | RDP, SSH, DCV allowed from Singapore RDP, SSH, DCV allowed from London
FSx Security | All allowed from 10.0.0.0/8 | Only members from AD group From London and Singapore
Deployment | Console + Cloud9 | TF Script

## Slide 21
Private subnet2
Private subnet1
Dyson To-Be – Inter-Connectivity within the AWS Parallel Cluster – Multi AZ
CloudWatch
Security Hub
Inspector
CloudTrail
KMS
IAM
SSO
Dir Service
HPC
AZ-1
AZ-3
Private subnet3
TGW
AZ-2
Identity, Security & Compliance
Secrets Mgr
FSx for ONTAP
S3
Cloud9
RDD NPR A/C
Ireland Region
Head Node (CentOS 7)
Scheduler,
C6i.2xlarge
Workstation (Windows)
NICE DCV Server
G4dn.8xlarge
Compute Nodes
Compute Nodes
Compute Nodes
Compute Nodes
Compute Nodes
Compute Nodes
Compute Nodes
Compute Nodes
Compute Nodes
Job Queues
DCV Client
DCV Session
Data Connectivity
Data
Data Upload
DCV Session
Submit Job
Send to Queue
Data Connectivity
Business User
Notes: Note:
The total cluster will be created in private subnets spanning across three AZs
Workstations, HeadNode will be connected to On-Prem network though SD-WAN, TGW and Domain join
Workstations: Windows 10, HeadNode: Ubuntu 20.04, On-Demand compute Node: ???
FSx Luster storage will be used
Job Scheduler Slurm will be used, however LSF is preferred
How many Job queues we should have?
Do we have any interface (i.e. similar to SOCA) to create the Workstation?
Is only One HeadNode is sufficient in the PoC phase?
Can we make it a single region, 3 AZ, without the LoadBalancer in PoC phase?
Onprem connectivity and Domain Join is required to connect the On-prem License server, NFS, PLM server
How to create the Nodes considering the Dyson domain join security requirement
What should be CIDR ranges? Is 255 IP range is OK for the PoC?
How many maximum compute node we are expecting to complete the given use cases, based on that we can ask Dyson to allow the CIDR ranges
How to do we scan the compute nodes against Qualys if that will come as a mandate?

## Slide 22
DCV Client
Users
Dyson To-Be – Inter-Connectivity within the AWS Parallel Cluster – Single AZ
CloudWatch
CloudTrail
KMS
IAM
SSO
Dir Service
HPC
TGW
Identity, Security & Compliance
Secrets Mgr
FSx for ONTAP
Ireland Region
Head Node
Slurm Scheduler
CentOS 7,
Compute Nodes
Compute Nodes
Compute Nodes
Compute Nodes
Compute Nodes
Compute Nodes
Job Queues
DCV Session
Data Connectivity
DCV Session
Submit Job
Send to Queue
Workstations
NICE DCV Server
Dyson on-premise
Notes: Note:
The total cluster will be created in private subnets spanning across three AZs
Workstations, HeadNode will be connected to On-Prem network though SD-WAN, TGW and Domain join
Workstations: Windows 10, HeadNode: Ubuntu 20.04, On-Demand compute Node: ???
FSx Luster storage will be used
Job Scheduler Slurm will be used, however LSF is preferred
How many Job queues we should have?
Do we have any interface (i.e. similar to SOCA) to create the Workstation?
Is only One HeadNode is sufficient in the PoC phase?
Can we make it a single region, 3 AZ, without the LoadBalancer in PoC phase?
Onprem connectivity and Domain Join is required to connect the On-prem License server, NFS, PLM server
How to create the Nodes considering the Dyson domain join security requirement
What should be CIDR ranges? Is 255 IP range is OK for the PoC?
How many maximum compute node we are expecting to complete the given use cases, based on that we can ask Dyson to allow the CIDR ranges
How to do we scan the compute nodes against Qualys if that will come as a mandate?

## Slide 24
DCV Client
Users
Dyson To-Be – Inter-Connectivity within the AWS Parallel Cluster – Two AZ
CloudWatch
CloudTrail
KMS
IAM
SSO
Dir Service
HPC
TGW
Identity, Security & Compliance
Secrets Mgr
FSx for ONTAP
Ireland Region
Job Queues
DCV Session
Data Connectivity
DCV Session
Submit Job
Send to Queue
Workstations (Windows)
Head Node (RHEL)
Scheduler
C6i.2xlarge
Dyson on-premise
Compute Nodes
Compute Nodes
Compute Nodes
Head Node (RHEL)
Scheduler
C6i.2xlarge
Send to Queue
Job Queues
Compute Nodes
Compute Nodes
Compute Nodes
Notes: Note:
The total cluster will be created in private subnets spanning across three AZs
Workstations, HeadNode will be connected to On-Prem network though SD-WAN, TGW and Domain join
Workstations: Windows 10, HeadNode: Ubuntu 20.04, On-Demand compute Node: ???
FSx Luster storage will be used
Job Scheduler Slurm will be used, however LSF is preferred
How many Job queues we should have?
Do we have any interface (i.e. similar to SOCA) to create the Workstation?
Is only One HeadNode is sufficient in the PoC phase?
Can we make it a single region, 3 AZ, without the LoadBalancer in PoC phase?
Onprem connectivity and Domain Join is required to connect the On-prem License server, NFS, PLM server
How to create the Nodes considering the Dyson domain join security requirement
What should be CIDR ranges? Is 255 IP range is OK for the PoC?
How many maximum compute node we are expecting to complete the given use cases, based on that we can ask Dyson to allow the CIDR ranges
How to do we scan the compute nodes against Qualys if that will come as a mandate?

## Slide 25
System requirements for PoC |  |  |  |  |  | 
Sl. No | Description | Environment | Instance Type | vCPU | RAM (GB) | Disk (GB)
1 | Head Node | NPR RDD | C6i.2xlarge | 128 | 256 | 1024
2 | Workstation-1 | NPR RDD | G4dn.16xlarge | 64 | 256 | 600
3 | Workstation-2 | NPR RDD | G4dn.8xlarge | 32 | 128 | 600
4 | Workstation-3 | NPR RDD | G4dn.8xlarge | 32 | 128 | 600
5 | Workstation-4 | NPR RDD | G4dn.8xlarge | 32 | 128 | 600
6 | Compute Node | NPR RDD | C6i.32xlarge | 128 | 256 | 1024
Dyson To-Be – Sizing Details

## Slide 26: Dyson To-Be – AWS SSO Authentication Flow
Notes: Note:
Can you skip the LoadBalancer in PoC phase?

## Slide 27
Dyson To-Be – Implementation
Cloud Engineer
Terraform Script
Cloud Engineer
Cloud9
Install Pre-requisites
Create the Config
Create SSH Key
Create Head Node
Create Workstation
1
2
a
c
b
d
f
Configure the WS
g
Users
3
Workstation (Windows)
G4dn.8xlarge
HPC Cluster
Scheduler,
NICE DCV
Storage, Compute
Job Queues
Configure the Cluster
e

## Slide 28
Dyson To-Be – Implementation
Cloud Engineer
Terraform Script
1
2
Cloud Engineer
4
Base Infrastructure
vpc, subnet, sg, key-pair, role, policy
Fsx NetApp ONTAP
FSx Installed & Configured
3
AWS Parallel Cluster
Cloud Engineer
Cloud Engineer
Parallel Cluster Installed and Configured
Create Workstation (EC2 Instance)
Parallel Cluster Installed and Configured

## Slide 29: Dyson To-Be – Security Rules
Notes: Note:
Can you skip the LoadBalancer in PoC phase?

## Slide 30: Dyson To-Be – Security Group
Workstations
On-Prem Servers
FSx for ONTAP
London Users
Singapore Users
Head Node
LDAP
/AD
LDAP/AD
Compute Nodes
Data Request
RDP, DCV Request
SSH Request
LDAP Request
On-prem Request
Submit Job
RDP & DCV
RDP &, DCV
SSH
SSH
Map Storage
Map Storage
Mount Storage
Domain Join
Domain Join
Directory Service Integration
HPC Apps Connects to on-prem servers
HPC Apps Connects to on-prem servers
All Traffic
Submit Job
Notes: Note:
Can you skip the LoadBalancer in PoC phase?

## Slide 31
rdd-npr-hpc-poc-1a-sn
Dyson To-Be – Terraform Plan to create infra for Cloud9
HPC VPC
eu-west-1a
Cloud9
NPR RDD A/C
Ireland Region
Notes: Note:
The total cluster will be created in private subnets spanning across three AZs
Workstations, HeadNode will be connected to On-Prem network though SD-WAN, TGW and Domain join
Workstations: Windows 10, HeadNode: Ubuntu 20.04, On-Demand compute Node: ???
FSx Luster storage will be used
Job Scheduler Slurm will be used, however LSF is preferred
How many Job queues we should have?
Do we have any interface (i.e. similar to SOCA) to create the Workstation?
Is only One HeadNode is sufficient in the PoC phase?
Can we make it a single region, 3 AZ, without the LoadBalancer in PoC phase?
Onprem connectivity and Domain Join is required to connect the On-prem License server, NFS, PLM server
How to create the Nodes considering the Dyson domain join security requirement
What should be CIDR ranges? Is 255 IP range is OK for the PoC?
How many maximum compute node we are expecting to complete the given use cases, based on that we can ask Dyson to allow the CIDR ranges
How to do we scan the compute nodes against Qualys if that will come as a mandate?

## Slide 32
rdd-prd-hpc-euw1-1b-sn1
rdd-prd-hpc-euw1-1a-sn1
Dyson To-Be – Terraform Plan to create infra for Cloud9
VPC
eu-west-1
PRD RDD A/C
Ireland Region
sg-rdd-prd-hpc-computenode
IAM
S3
Route53 Resolver
IAM Role, Policy
FSx for ONTAP
sg-rdd-prd-hpc-head
Head Node (RHEL)
Scheduler
C6i.2xlarge
Compute Nodes
Compute Nodes
Compute Nodes
Compute Nodes
Workstations (Windows)
sg-rdd-prd-hpc-workstation
Notes: Note:
The total cluster will be created in private subnets spanning across three AZs
Workstations, HeadNode will be connected to On-Prem network though SD-WAN, TGW and Domain join
Workstations: Windows 10, HeadNode: Ubuntu 20.04, On-Demand compute Node: ???
FSx Luster storage will be used
Job Scheduler Slurm will be used, however LSF is preferred
How many Job queues we should have?
Do we have any interface (i.e. similar to SOCA) to create the Workstation?
Is only One HeadNode is sufficient in the PoC phase?
Can we make it a single region, 3 AZ, without the LoadBalancer in PoC phase?
Onprem connectivity and Domain Join is required to connect the On-prem License server, NFS, PLM server
How to create the Nodes considering the Dyson domain join security requirement
What should be CIDR ranges? Is 255 IP range is OK for the PoC?
How many maximum compute node we are expecting to complete the given use cases, based on that we can ask Dyson to allow the CIDR ranges
How to do we scan the compute nodes against Qualys if that will come as a mandate?

## Slide 33
Dyson To-Be – High Level Architecture Diagram using AWS Parallel Cluster (AWS Reference Architecture)

## Slide 34
Dyson – High level Architecture Diagram with Multi-Account
Malmesbury
LDAP
/AD
LDAP/AD
Master Account
Production Account
NPR RDD Account
VPC-HPC-Dev
VPC-HPC-Test
VPC-HPC-Prod
Shared subnet from Network Account
AZ-1
AZ-2
Public subnet
NAT GW
Private subnet
AZ-1
Public subnet
NAT GW
Private subnet
AZ-2
Public subnet
NAT GW
Private subnet
AWS SSO
TCS Dev Center
Cloud9
SD-WAN
Test Account
TGW
TGW
AWS Managed AD
Client VPN
Connectivity
SD-WAN, Client VPN are connected to IGW
IGW, Cisco CSR deployed in Transit A/C
VPCs are connected through TGW & CSR
Authentication
AWS SSO based authentication
AWS SSO is integrated with MS AD
Domain join
Connect Workstations
Log-on to SSO Portal, then AWS Mgmt console, then Session Mgr to connect to Workstation
Alternatively, user can RDP to Workstations
Workflow
Users get into their Workstation
Browse the Head-Node Web Portal Load Balancer url, or Open the DCV session
The users will post job, and can visualize remotely via NICE DCV
POC Scope
Infrastructure creation for PoC
Leverage existing AWS Landing Zone
Leverage existing Active Directory, Domain
Data upload/migration & App deployment
Use case validation
Ireland Region
Two-Way Trust
Transit Account
Corp Subnet
Head Node
Scheduler
Web Portal
Analytical Dashboard
AZ-1
AZ-2
Workstation
NICE DCV
Workstation
NICE DCV
Compute Nodes
Compute Nodes
Head Node
Head Node
Cloud9
Workstation
NICE DCV
Workstation
NICE DCV
Compute Nodes
Compute Nodes
AZ-3
Public subnet
NAT GW
Public subnet
NAT GW
Public subnet
NAT GW
Head Node
Private subnet
Cloud9
Workstation
NICE DCV
Compute Nodes
Private subnet
Workstation
NICE DCV
Compute Nodes
Private subnet
Workstation
NICE DCV
Compute Nodes
TGW
Head Node
Head Node
Internet
Cisco CSR
Internet Gateway